## Slide 1
Optical Flow - Final Project
Team 7

## Slide 2: Outline
Optical Flow introduction
Kernel Architecture
Optimization
Timing & Resource Utilization
Result

## Slide 3: Optical Flow introduction

## Slide 4: Optical Flow introduction
Optical flow or optic flow is the pattern of apparent motion of objects, surfaces, and edges in a visual scene caused by the relative motion between an observer and a scene.

## Slide 5: Method
Lucas-Kanade algorithm
  The Lucas-Kanade optical flow algorithm is a simple technique which can provide an estimate of the movement of interesting features in successive images of a scene.
  Sparse (some pixels) or dense (all pixels)
  No longer state-of-the-art but still widely referenced

## Slide 6: LK Optical Flow
I(x,y,t) = I(x+dx,y+dy,t+dt)
Weighted least-square fit, assuming constant velocity in each section
Spatial derivative
Temporal image brightness derivative
𝄔
𝄔
Unknown motion vector in horizontal/vertical direction
Window function

## Slide 7: Constraint
1.The pixel intensity of the object between consecutive frames is constant
2. Similar motion between adjacent pixels

## Slide 8: Kernel Architecture

## Slide 9: Hardware diagram(8 stage)
Stage1 : Unpack
Stage2 : Gradient xyz
Stage3 : weight_y
Stage4 : wright_x
Stage5 : outer product
Stage6 : Tensor_y
Stage7 : Tensor_x
Stage8 : Compute flow

## Slide 10: Inputs and Outputs
Input : 5 Consecutive Frame
  1024 x 428 Pixel
Output : Optical flow Result
  Motion of X and Y
  FLO file
mp4 ->ppm -> kernel -> flo ->mp4

## Slide 11: Optimization

## Slide 12: Analysis
Resource Utilization
Latency

## Slide 13: Target
Memory customization
Memory bandwidth
Improve latency

## Slide 14: Image line buffer and window buffer
The kernels in optical flow have sliding window access patterns. As a result, line buffer and window buffer are introduced to exploit data reuse and reduce accesses to the next-level memory

## Slide 15: Streaming dataflow optimization
After using line buffer and window buffer, the kernels in optical flow have perfectly balanced throughput, and access data in strict sequential order. As a result, execution of all stages can be perfectly overlapped to form a very deep image processing pipeline

## Slide 16: Data packing
The hardware function kernel takes in five consecutive image frames. The corresponding pixels in the five frames are packed into a 64-bit integer for fast off-chip data transfer

## Slide 17: Pragma
1. pragma HLS array_partition
2. pragma HLS pipeline
3. pragma HLS dependence
4. pragma HLS data_pack
5. pragma HLS dataflow
6. pragma HLS STREAM

## Slide 18: Array Partition
Line Buffer and Window Buffer
Array Partition
  Multiple registers instead of one large memory
  Improves the throughput

## Slide 19: Pipeline
Read one pixel from input
Pipeline

## Slide 20: False Dependence

## Slide 21: Data Pack

## Slide 22: Pipeline II Violation

## Slide 23: Dataflow

## Slide 24: Stream
FIFO instead of RAM
more efficient communication

## Slide 25: Timing & Resource Utilization

## Slide 26: Pipelined Latency

## Slide 27: Pipeline Optimization

## Slide 28: Dataflow Optimization

## Slide 29: Stream Optimization

## Slide 30: Timming
Pragma Type | Latency (Absolute Max) | Timming(100 MHz) | (200 MHz)
None | 1.169 (sec) | 8.690 ns | 
Pipeline | 40.271(ms) | 8.657 ns | 
w/o Stream | 35.806 (ms) | 8.510 ns | 
w/o Datapack | 26.851 (ms) | 8.657 ns | 
Optimization | 4.496 (ms) | 8.657 ns | 5.527

## Slide 31: Compare
Utilization | Unoptimized | Optimization | Available
BRAM | 16770 | 135 | 280
DPS48E | 78 | 196 | 220
FF | 5388 | 33066 | 106400
LUT | 7376 | 26023 | 53200

## Slide 32: BRAM Utilization

## Slide 33: Stream FIFO

## Slide 34: Stream FIFO

## Slide 35: Resource
func/Utlis | BRAM | DSP48E | FF | LUT
gradient_xy | 8 | 8 | 835 | 1234
gradient_y | 42 | 42 | 2981 | 2200
gradient_x | 0 | 42 | 2203 | 1936
outer_product | 0 | 6 | 333 | 190
tensor_x | 0 | 36 | 1923 | 1748
tensor_y | 22 | 36 | 1960 | 1649
flow_calc | 0 | 24 | 21050 | 14358

## Slide 36: Result

## Slide 38
31.2 ms / frame
Blue : x direction
Purple : y direction

## Slide 39: Reference
[1] Wiki - Lucas–Kanade method
[2] Rosetta: A Realistic High-Level Synthesis Benchmark Suite for Software Programmable FPGAs, 2018
[3] Optical Flow Estimation
[4] Introduction To Optical Flow

## Slide 40: Github Link
https://github.com/yuweitt/Final-Project-Optical-Flow
Video
https://drive.google.com/drive/u/0/folders/1aZEH42efPpHFc-OHz4QsEv5FFpby9B18